## Slide 1: Virtual Reality Hardware
Capabilities and Limitations based on Human Perception

## Slide 2: Virtual Reality Headsets
Valve Index
  Latest High-end HMD in the market
  Released in 2019
  $999
Oculus Rift CV1
  HMD which HAJE owns
  Released in 2016
  Discontinued in 2019
    Succeeded by Oculus Rift S
  $599

## Slide 3: Human Perception: “Five Senses”

## Slide 4: Senses Ranked by Devoted Neurons in Brain
30%
8%
2%
<1%
~0%

## Slide 5: How Eyes Work
Relevant structures
  Pupil
  Lens
  Retina
    Fovea
Capabilities
  FOV: 200° X 130°
  Framerates: 60-120Hz
  Resolution: 30K X 20K dots
    Not uniform; denser near fovea

## Slide 6: Foveated Vision
Most cone cells are located within 2° from central axis (=fovea)
High-res image within fovea, low-res image outside of fovea
Human eyes overcome this by unconsciously jittering while gazing

## Slide 7: Depth Cues for Depth Perception
Accommodation
(Con-)vergence
Stereoscopic Vision

## Slide 8: Virtual Reality Headsets: Resolutions + Framerates
Valve Index
  1440 X 1600 per eye
  80, 90, 120, 144Hz available
Oculus Rift CV1
  1080 X 1200 per eye
  90Hz

## Slide 9: Virtual Reality Headsets: FOV
Field of view =How wide a human eye can see?
  Human: 200° horizontal, 130° vertical
  How to effectively cover human FOV?  Lenses

## Slide 10: Virtual Reality Headsets: FOV
Challenge: Lens distortion
  Lens distorts image behind it
    Pin-cushion distortion: lens stretches the image more at the edges
  Lens also distorts color (chromatic aberration)
Solution: Distortion correction
  HMD displays rendered images after applying inverse distortion
  Limitation: uneven pixel density

## Slide 11: Virtual Reality Headsets: Depth perception
Depth cues checklist
  ✔ Stereoscopic vision
  ✔ Vergence
  ✖ Accommodation
Vergence-Accommodation Conflict
  Causing discomfort, fatigue to eyes
  Limiting the length of sessions
  Possibly inducing headache
No depth-of-field effect (minor complaint)
  Every visual is located at the same focal distance
  Image may look unusual

## Slide 12: Solution to Vergence-Accommodation Conflict
Hardware solution: Multifocal display
Hardware solution: Varifocal display with focus-tunable lens

## Slide 13: Solution to Vergence-Accommodation Conflict
UI/UX solution
  Know your focal distance
    Due to lenses, optical distance between eye-display is farther than physical distance
    Oculus Rift CV1: ~2m
    Valve Index: ~2m
  Minimize vergence-accommodation mismatch as much as possible
    Frequent UI elements should be located around the focal distance
    Slow down the quick vergence changes
    Maximize the reliability of other depth cues
    …

## Slide 14: Coming Near Future: Foveated Rendering
Recall: Foveated vision
  Human eye can only see in Hi-res within very small area
Foveated Rendering
  More detailed image with less computing
  Eye tracking required to find the user’s viewing direction

## Slide 15: Head/Hand Tracking in Virtual Reality
Rigid bodies: 6 Degrees of Freedom
  3 Translational + 3 Rotational
Rotation tracking
  Gyroscope sensor
Position tracking
  Somewhat challenging

## Slide 16: Position Tracking Methods
Giving up
  Most mobile VR headsets (Oculus Go, Gear VR, Google Daydream View, …)
Tracking system
  Sensors detect patterns on the device, compute the position
    Low cost, high quality
    Predefined patterns  Limited trackable peripherals
    Limited field of view of sensors  Smaller tracking area
  Oculus Rift, PlayStation VR

## Slide 17: Position Tracking Methods
Lighthouse system
  Each station emits timed signal in space
  Peripherals detect the signal and compute positions
    Lighthouse does not need to connected to PC
    High quality, wide range of tracking  Room-scale
    Expensive, hard to install
    Reflective surface  Glitch
  HTC Vive, Valve Index

## Slide 18: Position Tracking Methods
Inside-out tracking
  Also called Simultaneous Localization and Mapping (SLAM)
  Headset captures the environment, infers its position (difference) in 3D space
    Low cost, no setup required
    Relatively low quality tracking
    Not working in dark
  Oculus Quest, Windows Mixed Reality

## Slide 19: Balance Sensing of Human
Recall: “Five Senses”
Gravity/acceleration sensing

## Slide 20: VR Sickness
Usually caused by sensory conflict
  Visual inputs of virtual motion vs Non-visual perception of self-motion
  Visually Induced Motion Sickness (VIMS)
Game designed that reduces VR sickness
  Mitigate perception of self-motion
  Minimize acceleration
  Introduce inertial reference frame (cockpit, nose)
  …

## Slide 21: Spatial Audio
Mono/Stereo/Surround audio
  Sound sources are located relative to head
Spatial audio
  Sound sources are locked in space  Immersive experience

## Slide 22: Sound Localization
Human can localize sound using 3 coordinates
  Azimuth, elevation, distance
  Similar to polar coordinates
Azimuth cues
  Duplex theory: cues from two ears
  Time difference (Interaural time difference, ITD)
  Relative amplitude (IID/ILD)
    Most notable in high frequencies
Distance cues
  Loss of amplitude, loss of high frequencies, …

## Slide 23: Sound Localization
Elevation cues
  Pinna filtering effect
    Shape of ears reflects sounds from each direction differently
    Exact effect varies by person
    Head-Related Transfer Function (HRTF)
      Mathematical model for the effect
      Requires specialized setup for precise measuring

## Slide 24: Sound Localization in VR
Spatial audio engines generates these cues from relative location of sound source
  Azimuth cues = strong
  Elevation cues = weak, varies from person to person  inaccurate perception
    Never solely rely on elevation cues

## Slide 25: VR Controllers
Oculus Touch (Oculus Rift CV1)
  6-DoF Tracking
    Patterns located on the rim
  4+1 usable buttons
    Thumbstick + 2 Face buttons
    Trigger (analog)
    Grip (analog)
  Finger detection  Immersion
  Multi-frequency vibration
    320*(1/N) Hz
    255 steps amplitude

## Slide 26: VR Controllers
Vive controller (HTC Vive)
  6-DoF tracking
  Symmetric design
  3+1 usable buttons
    Touchpad, Menu button
    Trigger (analog, dual-stage)
    Grip
  HD haptic feedback
    Microsecond haptic pulse
Vive tracker
  6-DoF tracking to any object

## Slide 27: VR Controllers
Valve Index Controllers
  6-DoF tracking
  4+2 usable buttons
    Thumbstick, track button, 2 face buttons
    Trigger
    Grip force sensor
  Finger tracking

## Slide 28: VR Controllers – Limitations
Lack of force feedback
  Recall:
  Constrained motion  Mismatch between virtual and physical hand
    Beads on wire
    Two-hand weapon (baseball bat)
  Weight, touching, pushing, …
    Haptic cues are limited (vibration)
    Maximize other cues (visual + auditory)

## Slide 29: Experimental VR Controllers
Leap Motion
  Full hand-tracking
  High-precision control

## Slide 30: Experimental VR Controllers
Nintendo LABO: VR Kit
  Task-specialized add-ons
  Rich tactile feedback

## Slide 31: Summary
VR games require extensive UI/UX design phase
  (What kind of experience will the game give to users?)
  How to minimize discomfort?
    VR sickness, eye strain, muscle fatigue, …
  How to maximize immersion?
    UI element placement, primary interaction, …
Need various research to answer such questions
  Hardware survey
  Case study
    Either good ones, or bad ones