## Slide 1: 3D Game Art Overview
#project_vr_something

## Slide 2: Game Development Process

## Slide 3: How 3D Graphics Work
Rig
Mesh
Texture
Skinning
UV Mapping
Animation Engine
Renderer
Posed rig
Mesh
Deformed mesh
Textures
(Lightings)
Rendered image
Shape of things
Pose parameterization
of moving things
Visual details of things

## Slide 4: How 3D Renderer Works
Virtual light
Virtual camera
Albedo
Specular
Occlusion
Normal
…

## Slide 5: How 3D Animation Works
Keyframe animation
Procedural animation

## Slide 6: 3D Game Art Pipeline
Modeling
Texturing
Rigging
Animation

## Slide 7: 3D Game Art Pipeline – Concept Art

## Slide 8: 3D Game Art Pipeline – Sculpting

## Slide 9: 3D Game Art Pipeline – 3D Scanning

## Slide 10: 3D Game Art Pipeline – Retopology

## Slide 11: 3D Game Art Pipeline – UV Mapping

## Slide 12: 3D Game Art Pipeline – Texturing

## Slide 13: 3D Game Art Pipeline – Rigging & Skinning

## Slide 14: 3D Game Art Pipeline – Animation

## Slide 15: Technical Challenges – Modeling
Good topology vs Bad topology
  Watertight
  Edge flow
  Extra edges near joints
  …
Polygon count

## Slide 16: Technical Challenges – UV Mapping
Minimize seams/distortion/overlap
Efficient layout

## Slide 17: Technical Challenges – Texturing
Material parameterization
  Physically-based rendering
  Non-photorealistic rendering

## Slide 18: Technical Challenges – Rigging & Skinning
Expressive vs Complicated
  General-case rig / special-case rig
  Reusable rig
Common artifacts
  Extreme bending  Bulging
  Extreme twisting  Candy-wrapper